## Slide 1: Economic assessment of electric vehicle fleets providing ancillary services
Eva Szczechowicz,
Thomas Pollok,
Armin Schnettler
RWTH Aachen University
Szczechowicz@ifht.rwth-aachen.de
SZCZECHOWICZ – DE – S6 – 0967

## Slide 2: Content
Motivation
Model description
  Technical and economic model
Charging strategies and technical results
Economic results
Summary and conclusions
SZCZECHOWICZ – DE – S6 – 0967

## Slide 3: Motivation
Potential for providing ancillary services to the market  (V2G services)
Possible earnings for vehicle owner or other market participants
Development of a model to simulate ancillary services with a electric vehicle fleet
Calculation of potential earnings
Consideration of relevant technical restrictions
SZCZECHOWICZ – DE – S6 – 0967
Notes: Other market partitioner such as an aggregator

## Slide 4: Content
Motivation
Model description
  Technical and economic model
Charging strategies and technical results
Economic results
Summary and conclusions
SZCZECHOWICZ – DE – S6 – 0967

## Slide 5: Model structure
Technical model
Vehicle specifications
  Driving pattern
  Battery size
  Consumption
Prequalification for ancillary markets
Charging infrastructure
Results
Required pool size for the fleet
Earnings for each vehicle
Simulation
Calculation of the required maximal pool size
EVs currently providing reserve energy based on historical data
Economic model
Reserve energy market
  Energy prices
  Capacity prices
Battery and battery degradation costs
Costs for conventional charging process (stock exchange)
SZCZECHOWICZ – DE – S6 – 0967
Notes: Technical assessment:
Simulation of the charging process of a fleet of EVs during the day
Consideration of technical restrictions
Economic assessment:
Calculation of possible benefits of providing ancillary services with a fleet of Evs determined in the technical part

## Slide 6: Parameters considered
Realistic driving pattern
  Study “Mobilität in Deutschland 2008”
Characteristic battery charging curve for Li-ion batteries
Reserve energy according to German prequalification
Infrastructure scenario:
  Connection power: 3.7 kW
  Charging places: At home and at work
SZCZECHOWICZ – DE – S6 – 0967
In 2010 | Primary reserve | Secondary reserve
Power | ± 2 MW | +/- 10 MW
Activation time | < 30 s | < 5 min
Duration | < 15 min | 30s – 1h
Availability factor | 100% | 95 %
Pooling | No | Yes

## Slide 7: Content
Motivation
Model description
  Technical and economic model
Charging strategies and technical results
Economic results
Summary and conclusions
SZCZECHOWICZ – DE – S6 – 0967

## Slide 8: Control strategies – Negative reserve
SZCZECHOWICZ – DE – S6 – 0967
Negative ancillary services
SOC<100%
Delay-Strategy
100%
SOC
t(delay)
t
Energy-Strategy
Target SOC
Combination of both strategies:
Energy+Delay-Strategy

## Slide 9: Pool size for negative reserve
The required pool size fluctuates over the day.
Around 55000 EV are necessary to provide 10 MW reserve energy.
The size of the pool is very high compared to the number of EV actually providing reserve energy.
SZCZECHOWICZ – DE – S6 – 0967
Monday Tuesday Wednesday Thursday Friday Saturday Sunday
Pool size – Energy
Providing EV - Energy
Pool size – Energy + Delay
Providing EV – Energy + Delay

## Slide 10: Control strategies – Positive reserve
Stochastic delayed charging process for every EV
Minimum state of charge (SOC)= target SOC
Assumption: Enough energy for the next trip is stored.
SZCZECHOWICZ – DE – S6 – 0967
Positive ancillary services
Bidirectional
Feed-in of storage energy
Unidirectional
Stopping of the charging process
SOC
100%
0
t
Start
Stop
Target
SOC
SOC
100%
0
t
Start
Stop
Target
SOC

## Slide 11: Pool size for positive reserve
High variations in the required pool size over the day
Smallest required pool for the bidirectional control strategy
Monday Tuesday Wednesday Thursday Friday Saturday Sunday
Negative Energy
Negative Energy+Delay
Positive Bidirectional
Positive Unidirectional
Required pool size
SZCZECHOWICZ – DE – S6 – 0967
Max 10MW
Min 10MW
Max 2MW
Min 2MW
Neg: „Energy“
59326
19605
11866
3921
Neg: „Energy+Delay“
50233
14514
10047
2903
Pos:
„bidirectional“
21712
7310
4343
1462
Pos: „unidirectional“
125621
3744
25125
749

## Slide 12: Content
Motivation
Model description
  Technical and economic model
Charging strategies and technical results
Economic results
Summary and conclusions
SZCZECHOWICZ – DE – S6 – 0967

## Slide 13: Results – Economic assessment
Input data
  Demand of reserve energy and historical energy prices from 2009
  Costs for energy consumption based on prices from the energy exchange
  Aggregator executes the pooling of EV
  Battery investment cost: 500€/kWh
Results
  Primary reserve: max 200 € per year and EV
  Secondary reserve: max 137 € per year and EV
Earnings are highly dependent on
  Chosen strategy and used target state of charge
  Battery investment cost
SZCZECHOWICZ – DE – S6 – 0967
Source: J. Link, et al., “Optimisation Algorithms for the Charge Dispatch of Plug-in Vehicles based on Variable Tariffs”, Fraunhofer ISI

## Slide 14: Variation of target SOC and battery costs
Monthly earnings per EV
Target SOC varies between 60%-97.5%
Two scenarios for the battery investment costs
  500€/kWh
  200€/kWh
Highest earnings for ancillary services can be reached with a target SOC of more than 90%.
SZCZECHOWICZ – DE – S6 – 0967

## Slide 15: Content
Motivation
Model description
  Technical and economic model
Charging strategies and technical results
Economic results
Summary and conclusions
SZCZECHOWICZ – DE – S6 – 0967

## Slide 16: Summary and conclusions
A fleet of electric vehicles can be used to provided positive and negative reserve energy
The pool sizes varies significantly depending on the control strategy
Earnings for a single EV per year have been calculated
  Primary reserve: max 200 € per year and EV
  Secondary reserve: max 137 € per year and EV
Primary reserve possesses the highest earning potential
Many different cost aspects have to be considered
The unidirectional strategy for positive reserve is preferable as long as the battery degradation costs are high.
SZCZECHOWICZ – DE – S6 – 0967
Notes: EV können mit Hilfe von Ladestrategien an Regelmärkten teilnehmen und ebenfalls andere Systemdienstleistungen erbringen
Mögliche Einnahmen am Regelenergiemarkt
    → Primärregelreserve bis zu 16,60€ / Monat / EV
    → Sekundärregelreserve bis zu 11.45€ / Monat / EV
Sinkende Batterieinvestitionskosten erhöhen das Einnahmepotential
Durchdringungsraten zur vollständigen Deckung des deutschen Regelenergiebedarfs werden bis 2030 nicht erreicht
Konkurrenz mit anderen Anbietern hält die Preise auf einem höheren Niveau als die Grenzkosten der EV-Flotte

## Slide 17: Thank you for your attention!
Eva Szczechowicz
RWTH Aachen University
Szczechowicz@ifht.rwth-aachen.de
www.ifht.rwth-aachen.de
SZCZECHOWICZ – DE – S6 – 0967

## Slide 18: Relevant aspects for an economic assessment
+
Earnings
(EBIT)
Revenues from reserve energy markets
Vehicle modification
Battery degradation costs
Communication infrastructure
Aggregator costs
Regulatory framework
...
-
Revenue
Cost
$
SZCZECHOWICZ – DE – S6 – 0967

## Slide 19: Results – Changed time slot duration
Calculations before: time slices 24h
Power: 10 MW
SZCZECHOWICZ – DE – S6 – 0967
Positive Bidirectional
Positive Unidirectional
Negative “Energy+Delay”
Size of the pool
Time slice (2h blocks)
Low advantage for the negative and positive bidirectional control strategy
The amount of positive reserve energy using unidirectional control strategy can be increased significantly during the most hours of the day
Notes: 10 MW
2h slots

## Slide 20: Battery degradation cost
Source: J. Link, et al., “Optimisation Algorithms for the Charge Dispatch of Plug-in Vehicles based on Variable Tariffs”, Fraunhofer ISI

## Slide 21: Revenues for reserve energy
Monthly costs and revenues for a single electric vehicle providing 10 MW secondary reserve energy
Low target SoC: 50%
Energy cost: EEX market price
Battery: 500€/kWh

## Slide 22: Backup
t
I(t)
U(t)
t
SoC(t)
P(t)
Current and voltage characteristics of a charging process
High voltage (Final condition)
Reduced power demand for charging
Characterisitcs of a 9kWh Lithium Ion battery

## Slide 23
Capacity price
Energy price