## Slide 1
Ignasi Cairó – SP – Session ….. – 0342
Implementation of a test microgrid in Barcelona

## Slide 2: Catalonia Research Institute of Energy
Power Electronics
Bioenergy
Advanced Materials
Offshore Wind
TECHNOLOGICAL AND RESEARCH AREAS
Zero Emission Buildings and cities (NZEB)
Reference Area: ENERGY EFFICIENCY
Technological and Knowledge Areas:
Lightning
Microgrids and Electrical Vehicle

## Slide 3: Components of the microgrid
  Real systems: photovoltaic generator (2 x 2.5 kW), Urban windmill (2 x 1 kVA), lithium-ion battery, ultracapacitors and flywheel storage (5 kW), PEV chargers (3.7kW, 50kW & 5 kWV2M);
  Semi-emulated systems: Wind emulator (SCIM) and real generator (SCIG, DFIG, PMSG) (5 -5.5 kW)
  Emulated systems: Photovoltaic, Wind power, battery (4 kVA), linear and non-linear load (100 kVA), Power Grid (200 kW);

## Slide 4
Emulated systems
Real Systems
EV charging
Power Balance:

## Slide 5: Hybrid uG concept
DC
DC
At the hybrid microgrid, it is possible to test either emulated and real DER devices

## Slide 6: Operating the microgrid
Control algorithm can handle centralized and distributed control. Independent control P/Q & €

## Slide 7
Power electronics converters are used to interface energy sources and Energy Storage Systems (ESS), between them and the grid

## Slide 8
4 batteries are considered: Lead-acid, Li-ion, Ni-Cd. Ni-Hidrur Metal. Also Supercaps & Flywheel

## Slide 9
  IEC 61850 from iNode to iSocket (Ethernet)
  Bus CAN from iSocket to converter physical variables,
  Modbus Ethernet network between measurement equipment.
Also developing; CHAdeMO, PLC, zigBee, 3G (GSM-UMTS)
Communications network is established in the uG

## Slide 10
We must provide communications in the power electronics  iNode + iSocket
IEC 61850 one possibility

## Slide 11: The IEC 61850 standard
The IEC 61850 in an international standard related with communications in Automation Systems for Substations (ASS).
In 1994, Technical Committee 57 of the IEC started the IEC 61850, taking as a reference the Utility Communications
First protocol published at 2001. Today, the standard has already been extended to DER and hydro plants.

## Slide 12: Control algorithm

## Slide 14: Monitoring the microgrid
http://www.irec.cat/index.php/ca/els-projectes/19-projectes-electronica-de-potencia

## Slide 15
Thank you for your attention.
Questions ??