## Slide 1
Douglas Wilson
Psymetrix Ltd, UK
D. Wilson – UK – Session 4 – Paper ID 0497
Connection and Management of DG using Phasor Measurements and DMS
Eric Goutard
Alstom Grid, France
Contributions gratefully acknowledged from
Avnaesh Jayantilal and John Sell, Alstom Grid, US

## Slide 2: Introduction
Synchrophasor measurement background
Integrated Distribution Management Systems (IDMS)
Autonomous & Centralised DG control

## Slide 3: Synchrophasor System Structure
C37.118 PMU/PDC Data Streams
IEC 60870-5-104
Client Applications
DMS Integration
Autonomous Control
Synchrophasor Applications
  Increase energy delivery
  Improve reliability
  System analysis
  Manage renewables
Standards published 1995, 2005
Extensive use in transmission

## Slide 4: Synchrophasor Measurement
Full per-cycle detail
GPS
Timestamp
Phase
Magnitude
Synchrophasors: Key Features
  Synchronised V&I measurements
  50/60Hz data captures dynamics
  3-phase measurements
  Real-time streaming
1
2
3
4
With PMUs, segment is fully observed from 2 locations, all 3 phases

## Slide 5: Integrated Distribution Management System
DMS Model-Based Analytics Enable Distribution Optimization
  Fault Location & Service Restoration Reduce Outage Time by 30%
  Reduce System Losses by 3-5%
  Peak Load Shaving of 5%
3-phase Power Flow Analysis
  Control Centre View
  Voltage and Thermal Management
  Safety and Reliability
Integrated SCADA and Outage Management

## Slide 6: DERMS Integration with Integrated DMS Distributed Energy Resource Management (DERMS)
Equipment
Models
GIS, Graphical
Editor
Customer
Model (CIS)
Analysis &
Optimization
Outage
Management
Network View
Network Operations
User Interface
Network Operations
Model
Call
Center
System
Simulator
Automated
Metering (AMI)
e-terrascada
System
Switching
Operations
Workforce
Management
Distribution
Automation
DR, DG -
DERMS
PMU Benefits
Model Verification
State Estimation
Load Flow / Control

## Slide 7: Distribution Network Modelling
HV-connected PMUs to define the boundary conditions: subsystem can be assessed independently.
Change of angle relative to the change of currents can be used to identify the generator or load.
Effects of common-mode events on the load and generation can be observed.
More generation capacity can be made available by determining the true limits of secure operation

## Slide 8: Distribution Connections
Increase capacity by constraining angle:
Manage multiple constraints
Simple control logic
Minimal comms
Generalised connect & manage
Applicable to Loss-of-Mains solution
Marginal reduction of capacity factor
More capacity
More energy
Notes: [Key points]
Angle differences reflect the stress of the grid . This concept can be applied in a mashed system (distribution systems)
Windfarm optimal dispatch control based on angle difference measurements (Actively Managed Connection)
Increasing of the Capacity Factor
[ACAM]

## Slide 9: PMU-based Dynamic Line Ratings
Enable More Transfer Capacity

## Slide 10: Conclusion
Central control benefits from PMU inputs
Autonomous control with PMUs
  Reduced complexity
  Ramp control / trip as required
  Generalised methods
Co-ordinated central & distributed control
Autonomous
Control
Centralised Management