## Slide 1: Trend of Distribution Network in Shanghai
SMEPC
6-9 June 2011
May 23

## Slide 2: 1. Overview of Distribution Network in Shanghai
Fundamental Data
  Service Area, 6600 km2
  Meters in the Service Area, 8M
  10kV Substations, 9533
  10kV Pad Mounted Trs, 29344
  10kV Pole Mounted Trs, 49216
  10kV OHL, 18439 km
  10kV Cables, 27604 km
  LV OHL, 31474 km
  LV Cables, 24347 km

## Slide 3: 1. Overview of Distribution Network in Shanghai
Power Consumption and Peak Load
  Consumption
  Peak Load
  Load Density
Chart: 
| 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0
Peak Load MW | 12351 | 13616 | 15006 | 16682 | 19543 | 21208 | 22432 | 23799 | 26212
Power Consumption TWh | 65.471 | 74.597 | 82.144 | 92.265 | 99.015 | 107.238 | 113.822 | 115.338 | 129.587
2010 | Core | Outer | Suburban
Density MW/km2 | 40 | 12.7 | 2.3
Area km2 | 116 | 540 | 4340

## Slide 4: 1. Overview of Distribution Network in Shanghai
Feature of The Network
  OHL Network
  Cable Network
Coverage Ratio of DA @2010
  DA without Self-healing, 30.90%
  DA with Self-healing, 1.46%
Cable Network
OHL Network

## Slide 5: 1. Overview of Distribution Network in Shanghai
SADI(min) & SAFI(times)
Chart: 
| 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0
SAFI | 0.495 | 0.455 | 0.469 | 0.41 | 0.372 | 0.333
SADI | 148.98 | 139.44 | 121.2 | 114.96 | 102.12 | 92.16

## Slide 6: 1. Overview of Distribution Network in Shanghai
Factors of Blackout @2010
Chart: 
| Failure | Maintenance | Infrastructure | New Customer Conect-in | City Infrastructure
Percentage | 14800 | 11291 | 33567 | 13984 | 10953

## Slide 7: 2. The Main Influence as SmartGrid to Be Introduced
Interactive Experience on Demand Side & DR
Higher Reliability
Connect-in of DG & DS
Infrastructure of EV
Smart Distribution and Power Consumption

## Slide 8: 3. Solutions We Will Adopt
Wind Mill
Solar
Mill
V2G
Power Storage
PQ Monitoring
AMI
UHVDC
iS/S
iBuilding
DA
TCM
iCommunity
iDispatching
Pilot Project at Shanghai EXPO 2010

## Slide 9: 3. Solutions We Will Adopt
High Reliability
  DA Criteria issued by SGCC
  DG and DS
  Micro-Grid
  TCM

## Slide 10: 3. Solutions We Will Adopt
Infrastructure of EV Service
  Public Transportation
  Personal EV
  Predication of the Next Five Yrs

## Slide 11: 3. Solutions We Will Adopt
Demand Side Application
  Smart Metering
  Smart Building and Community
  DR and Virtual Power Plant

## Slide 12: 3. Solutions We Will Adopt
Communication Infrastructure
  Cost of Communication Infrastructure
  OPLC (Optical Fiber Composite Low-Voltage Cable)
  How to Cope with the Huge Investment of Communication Infrastructure

## Slide 13: 3. Solutions We Will Adopt
Power Quality
  The Impact Factors
  PQ Monitoring System
  Solving the Power Pollution

## Slide 14: 4. Challenges
The END
Cost
Policy
Market