## Slide 1: Collecting PQ Economic Data
CIRED 2011
Round Table 2b
Frankfurt

## Slide 2: If around 1900 power failed for one minute
it was dark for one minute
If the power failed for one second
it was dark for one second

## Slide 3: If around 1950 power failed for one second
it was dark for three seconds

## Slide 4: If power fails today for only 50 ms
data gets lost,
the PC has crushed,
it takes minutes or even hours to resume normal operation.
Morals: Power must never ever fail, not even in case of a power failure!

## Slide 5: Reliability / VQ damage functions

## Slide 6: Percieved reliability level
Generally: the higher the reliability level, the more severe the impact of an interruption will be.
  A study in Nepal showed that 38% of residential consumers considered the number of interruption to be “low” or “very low” although the average number of outages was 4 a week.
  50% of the interviewed residential consumers in Brazilian valued the quality of service provided as “good” although half of these consumers experienced at least one interruption a week.
In most Western countries such interruption frequencies would not have produces such high consumer satisfaction ratings.
  Within the NL a street had 6 interruptions in one year.
  This was not accepted and caused heavy protests.
KEMA 2005

## Slide 7: Comparison of interruption costs
Source: Regulation beyond price (2005), National Technical University Greece
KEMA 2005

## Slide 8
Leonardo Polish seminar
2003 questionnaire
During seminars the participants were requested to fill up the questionnaire.
Main targets for the survey were:
PQ awareness
PQ threats – ranking of problems, solutions
Electricity supplier user relations
Leonardo campaign appraisal.
The survey was inspired by AGH and executed together with PCPM
Out of more then 1000 seminar participants totally 307 filled up the questionnaire. Respondents filled up questionnaire during seminar - 97% and in a few cases sent them after going home.

## Slide 9
Survey results (1)
15,3%
0,7%
28,0%
20,5%
35,5%
No answer
Not applicable
Services or other
Industry
Electrical sector - mostly utilities
Occupation

## Slide 10
4,2%
7,2%
7,8%
9,4%
9,8%
44,3%
7,2%
10,1%
No answer
Difficult to say
Every day or more freqently
Once a week
Once a month
Few times a year
Once a year
Very rarely or never
PQ problem frequency
Survey results (2)

## Slide 11
3,3%
85,3%
8,1%
3,3%
No answer
More important
Equally important
Less important
PQ today and 10 years ago
Survey results (3)

## Slide 12
4,2%
70,0%
18,6%
7,2%
No answer
Better
Similar
Worse
PQ guaranted by the supplier today and 10 years ago:
Survey results (4)

## Slide 13
Cost of one single short interruption in your company
13,4%
3,6%
4,6%
7,2%
7,8%
4,9%
50,5%
8,1%
No answer
>100000 PLN
<100000 PLN
<10000 PLN
<1000 PLN
<100 PLN
Difficult to say
No cost at all
Survey results (5)

## Slide 14
Causes of main PQ problems
0,00%
10,00%
20,00%
30,00%
40,00%
50,00%
No answer
Interruptions < 1 min.
Interruptions > 1 min.
Voltage dips and swells, transients
Harmonics
Flicker / frequent voltage fluctuation
Voltage value
Voltage unbalance
fFrequency changes
instalation itself (e.g. cable downsizing, faulty protection, earthing)
Survey results (6)

## Slide 15
Main sources of PQ problems
0,00%
10,00%
20,00%
30,00%
40,00%
50,00%
No answer
Converters, VSDs
UPS
Computers (electronics)
Lighting
Motors (e.g. during start up)
Welding, melting (fluctuating load)
Other
Survey results (7)

## Slide 16
Loads most sensitive to PQ deterioration
0,00%
10,00%
20,00%
30,00%
40,00%
No answer
Converters, VSDs
UPS
Computers (controls)
Capacitors
Motors
Switches; contactors and relays
Other
Survey results (8)

## Slide 17
PQ mitigation equipment in your company
0,00%
10,00%
20,00%
30,00%
40,00%
50,00%
60,00%
70,00%
No answer
No equipment
Stanby generator
UPS
Harmonic filtration
Overvoltage protection
Other
Survey results (9)

## Slide 18
Desired information on the equipment nameplate
0,00%
10,00%
20,00%
30,00%
40,00%
50,00%
60,00%
No answer
Immunity to
short interruptions
Immunity to
voltage distortion
Immunity to dips
and swells
Emissions level
Survey results (10)

## Slide 19
Desired supplier guaranteed PQ parameters
0,00%
10,00%
20,00%
30,00%
40,00%
50,00%
60,00%
70,00%
No answer
No. and time of interruptions
Voltage distortion
No. of dips and swells
Flicker
Unbalance
Voltage value
Frequency
Survey results (11)

## Slide 20
Investigating relations between answers to questions – hypotesis checks (1)
Independent variable | Correlation | Dependent variable
Frequency of PQ problem occurence | (+)→ | Voltage value as the main cause of PQ problems
Frequency of PQ problem occurence | No | Other PQ disturbances as the main causes of PQ problems
Frequency of PQ problem occurence | (-)→ | Utility contacted primarily when experiencing PQ problems
Frequency of PQ problem occurence | (+)→ | Own technical staff contacted primarily when experiencing PQ problems
Frequency of PQ problem occurence | (-)→ | Supplier is very formal – relates to contract only and is not helpful
Frequency of PQ problem occurence | (+)→ | User is interested in higher prices of electricity at improved level of PQ

## Slide 21
Independent variable | Correlation | Dependent variable
Cost of single short interruption | (+)→ | Supplier is responsible for main PQ problems
Short power interruption as the main PQ problem | (+)→ | Cost of single short interruption
Number of selected causes of PQ problems | (+)↔ | Number of applied soultions of PQ problems
Investigating relations between answers to questions – hypotesis checks (2)

## Slide 22
Independent variable | Correlation | Dependent variable
Harmonics as the main PQ problem | → No No → | Equipment which is the main source of PQ problems Converters and VSDs UPS Computers and electronics Lighting
Harmonics as the main PQ problem | ←(+) | Harmonic filtration as the PQ solution
Investigating relations between answers to questions – hypotesis checks (3)

## Slide 23: LPQI online survey Survey - pilot

## Slide 26
It is hard to estimate the costs of data and experimental results losses due to the shutdowns of PCs and other electronics equipment.
We have our own power generation and even export to the public network. But serious disturbances in the grid, like short circuits, can also affect us because the Island Operation reaction is not 100 % effective. But I have put these situations in Question 8 about voltage dips.
less than dips I hope (high reliability of the Belgian HV MV networks)
In cases involving interruptions, we did not measure interruption costs
Customer are notified of planned switch outs. 3rd party cable hits major problem.
It is hard to estimate the costs of data and experimental results losses due to the shutdowns of PCs and other electronics equipment.
The teaching and research is affected
In some cases analysed the cost by each event was about 20.000 Euro
depending on the size of company, various investigations have revealed losses from 1000 to 150000 Euro!
I do not think voltage dips are the cause of big losses in my company

## Slide 27
Our equipment and electrical network are normally oversized. Because it is usual in process industry, and short circuit powers are very high, etc. So we don´t notice directly the costs of harmonics.
Comes for us more and more important to find global economical solutions
In an industrial illumination system using halide lamps the solution to harmonic problem cost more than 20.000 Euro
one case involved loss of PF capacitors, but generally harmonics are seldom the real issue (I know, contrary to popular belief!).

## Slide 28: LPQI Survey PQ cost indices (industry)
 | Total cost per kWh €/kWh | Total cost per kW peak €/kW | Total cost per turnover (ratio) | Total cost per electricity bill (ratio) | Total cost per employment €/employee | Cost / kWh dip & short interruption €/kWh | Cost / kWh long interrupt. €/kWh | Cost / peak kW dip & short interrupt. €/kW | Cost per peak kW long interruption €/kW
Mean | 0,625 | 730,37 | 0,0374 | 7,530 | 8158 | 0,1352 | 0,0802 | 147 | 323
Std. Error of Mean | 0,459 | 298,24 | 0,0089 | 5,330 | 2995 | 0,0922 | 0,0469 | 57 | 260
Median | 0,031 | 95,57 | 0,0109 | 0,413 | 1218 | 0,0098 | 0,0012 | 28 | 4,18
Std. Deviation | 2,939 | 1909,72 | 0,0574 | 34,163 | 19181 | 0,5903 | 0,3008 | 371 | 1670
Variance | 8 | 3 647 060 | 0,0030 | 1 167,000 | 367 922 790 | 0,3490 | 0,0910 | 137 717 | 2 789 088
Minimum | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Maximum | 18,861 | 10 681 | 0,2375 | 218,552 | 113 638 | 3,7720 | 1,7090 | 1 771 | 10 681

## Slide 29: LPQI - Frequency of PQ events
Frequency of PQ disturbances | number of events |  |  |  | annual %
 | Voltage dips | Short interruptions | Long interruptions | Surges and transients | Harmonics
Industry | 15,7 | 6,9 | 2,2 | 13,0 | 9,0%
Services | 7,7 | 5,4 | 2,1 | 6,7 | 7,5%
Average | 13,2 | 6,4 | 2,2 | 11,3 | 8,5%
Notes: The frequency of PQ events reported in the survey can be characterized shortly as follows. On average the MAIFI that has been measured by this Survey is approximately 6; this is 3 times bigger than SAIFI. The number of recorded voltage dips, that is identified by the respondents, is approximately twice the number of short interruptions (MAIFI). This ratio is somewhat less for the services sectors.

## Slide 30: Technical conclusions from LPQI survey
Although there is no significant correlation between value of solutions investments and real PQ cost, a strong correlation exists between investment in PQ solutions and the hypothetical (mitigated) to real (unmitigated) PQ cost ratio.
One side effect of UPS’ use is the increased cost of harmonics.
There is rather poor correlation between perceived consequences of PQ and PQ solutions used. In other cases relation of these is difficult to justify from technical point of view. This somehow proves certain suboptimum in choosing PQ solution in particular case.
PQ solutions for all sectors covered [extrapolated from the €300 million identified by the Survey] ~ €13bn or less than 10% of PQ losses & 1% of the average estimated net profit.
In general “Services” apply a higher frequency of different PQ solutions than found in “Industry”. “Industry” tends to favour less costly, but also less universal - more tailored solutions whenever possible.
Notes: Although there is no significant correlation between value of solutions investments and real PQ cost, a strong correlation exists between investment in PQ solutions and the hypothetical (mitigated) to real (unmitigated) PQ cost ratio. Apart from specifying real PQ cost of wastage, respondents also defined those hypothetical costs that would be the potential losses and risk avoided by power systems that had been immunized against the PQ disturbances under review. The increase in the ratio between hypothetic and real (mitigated / unmitigated) is particularly visible in case of UPS.
One side effect of UPS’ use is the increased cost of harmonics. This can be explained by suboptimal use of UPS systems that are based on diffused small units without active power wave modulation, which in turn generates significant input current distortion.
There is rather poor correlation between perceived consequences of PQ and PQ solutions used. In other cases relation of these is difficult to justify from technical point of view. This somehow proves certain suboptimum in choosing PQ solution in particular case.
PQ solutions for all sectors covered [extrapolated from the €300 million identified by the Survey] ~ €13bn or less than 10% of PQ losses & 1% of the average estimated net profit.
In general “Services” apply a higher frequency of different PQ solutions than found in “Industry”. “Industry” tends to favour less costly, but also less universal - more tailored solutions whenever possible.

## Slide 31: PQ cost summary

## Slide 32
Mitigation of voltage dips
Small UPS
CVT
Voltage regulator
Large static UPS
Rotary UPS
Dynamic voltage
restorer (DVR)
Grid upgrade
Philosophy of selecting PQ solution
Notes: The last stage, 4, is to protect the whole plant by, for example a grid upgrade, a dual grid supply or perhaps a dynamic voltage restorer. Here we are talking about hundreds of thousands of Euro upwards.

## Slide 33: PQ consequence / solution correlation
PQ consequence | PQ solution | Relation
Relays and contactors nuisance tripping | Harmonic filter (passive) | significant
Noise interference to telecommunication lines | Multiple independent feeder | significant
Motors or process equipment are damaged | Shielding and grounding | significant
Motors or other process equipment malfunctions | Back up generator | very significant
Loss of synchronization of processing equipment | Surge protection on key pieces of equipment | significant
Loss of synchronization of processing equipment | Harmonic filter (passive) | very significant
Circuit breakers or RCD’s nuisance tripping | Line conditioner or active filter | significant
Circuit breakers or RCD’s nuisance tripping | Back up generator | significant
Capacitors bank failure | Shielding and grounding | very significant

## Slide 34: PQ investment effectivenes

## Slide 35: Perceived presence of disturbances

## Slide 36: (Perceived) PQ problem source

## Slide 37: (Perceived) PQ consequences

## Slide 38: Equipment being affected

## Slide 39: PQ solutions (perceived)

## Slide 40: PQ measurement

## Slide 41: PQ blame

## Slide 42: PQ investment / PQ cost per turnover

## Slide 43: PQ solution load coverage

## Slide 44: Power Quality Solutions adopted
“Services” sectors tend to invest more into original designs
“Industry” sectors often have to adapt existing possibly older installations to cope with current demands
Sectors that cannot allow for power interruptions tend to design reliability & resilience into their systems.
Notes: The broad picture that we have found is that “services” sectors tend to invest more before the event into design systems that ensure greater reliability and resilience for their electrical power systems; the in a sense “older” industrial sectors for understandable reasons are often faced with having to adapt and upgrade existing electrical power installations to modernize them and mitigate the lack of reliability they experience from the existing system design.
But then we should now be saying that these organisations, being so dependent on continuity of electrical power supply for their very survival in this increasing demanding world, through correct and systematic measurement are aware of what the power quality issues are within their electrical installations and are therefore ahead of the game in applying correctly defined and proportioned solutions to avoid them.
We have to say that unfortunately we did not find the result that we had hoped for – rather and paradoxically the reverse seemed truer.

## Slide 45: Questionnaire - collecting economic data

## Slide 46: The questionnaire – pilot + attributes

## Slide 47: Scenarios

## Slide 48: The questionnaire – process

## Slide 49: The questionnaire – process 2

## Slide 50: The questionnaire – non process oriented

## Slide 51: CIGRE C4.107 Documents repository
All together > 400 documents

## Slide 52: Documents – Search; „voltage” or „dips”

## Slide 53: Conclusion - The reasons for investigating the cost of PQ
to build awareness of the potential magnitude of PQ costs which may affect the productivity of the company
while statistics and previous experiences are helpful, no two companies, even when operating in the same sector, will be equally vulnerable to PQ disturbances
as PQ becomes subject to contract between a user and a supplier, the cost of PQ needs to be quantified to establish the so-called ‘Willingness to Pay or Accept’ as is a measure of a value of improved PQ for which the user is going to pay a premium or receive compensation for inadequate quality
in case of failure caused by a PQ event for which the supplier is contractually liable, the amount of compensation will need to be determined. A previous cost survey will help to establish the methodology, allowing a prompt and accurate determination of the amount.
awareness of the cost of PQ will help to minimise it. Once their potential contribution is recognised, many small and simple incremental improvements are possible without significant investment.
Finally PQ cost knowledge is a tool for regulators to set incentives for suppliers. The benefit should retain for the whole society but primarily for energy sector it should be adjusted so, as the retention period is sufficiently long to encourage companies to undertake investments
  Setting limits
    Based on the actual figures during a sufficiently long historic period
    Using some form of benchmarking (relative to the performance of other companies) or using a reference network model